## Slide 1: Development in TIPS RAS of novel advanced processes for conversion of gaseous feedstock and polymer wastes to value-added chemical products
INOVACE 2013

## Slide 2
Innovation technologies for unconventional chemical feedstock transformation
New technology for synthesis gas production
New technology for production of olefins or gasoline from natural , associated or biogas
New technologies for synthesis gas transformation in slurry systems
Novel processes for polymer waste to fuel transformation

## Slide 3: OXIDATION OF NATURAL GASES TO SYN-GAS IN REACTOR SYSTEM WITH FEEDING OF OXIDANT AND HYDROCAARBON IN DIFFERENT REACTORS
Natural or associated
gas,
Biogas
H2 + CO
(syn-gas)
Air
Nitrogen
Metal oxide (MeO)
Metal (Me)
Catalyst regeneration:
O2 + 2Me0 → 2MeO
Syn-gas formation reactor
Regenerator
Conversion hydrocarbons in syn-gas:
CnHm + nMeO → nCO + ½m H2 + nMe
CO2+CH4 = 2CO+2H2
ADVANTAGES OF NEW TECHNOLOGY OF SYNGAS PRODUCTION:
44 % less capital costs and 16% less syngas production costs in comparison to traditional steam reforming;
Processing of associated petroleum gas with a wide range of C2-C4 hydrocarbons and CO2 into synthesis gas ;
Using air as an oxidant without dilution of syngas with nitrogen;
Elimination of the formation of explosive oxygen-hydrocarbon mixtures;
Low rate of catalyst deactivation due to coke removal during regeneration;
Production of considerable amounts of pure nitrogen

## Slide 4
PROPYLENE (TILL 60%)
ETHYLENE (TILL 40 %)
NEW NANOSTRUCTURATED CATSLYST
BASED ON ZSM-5
DIAGRAM OF OLEFINS (ETHYLENE AND PROPYLENE) SYNTHESYS TIPS RAS
NATURAL GAS
SYNGAS
Men+
Men+
Men+
0,5-0,7 ть
Catalyst production on
Industrial scale
DME synthesis
Olefins production
Gasoline or naphtha production
The 2600 м3 of natural or associated gas gives 1 t of olefins
The yield of gasoline is 40- 50000 t per 1 mln. m3 of gas.
Notes: 4

## Slide 5
DESIGN OF PILOT PLAN

## Slide 6
Process | Conversion | Olefin esynthesis |  |  | С2-С4 olefins, % | Selectivity | 
 |  | Катали-затор | Т,оС | % |  | С2= | С3=
Пиролиз | 70 | - | 1000 | >99 | 47 | 31 | 17
Mobil | 50-70 | ZSM-5 | 350-400 | 47-75 | 26-56 | 7-24 | 20-28
UOP/Norsk-hydro | 70 | SAPO-34 | 450 | До 100 | 75-90 | 38-50 | 32-36
Lurgi (DME) | 70 | ZSM-5 | 430-450 | 99 | >69 | 0 | 70
Van Dijk (DME) | - | SAPO-34 | 450 | 70 | 49 | 70 | 0
DME TIPS | >80 | ZSM-5 | 340-450 | 95-100 | 80-88 | 30-50 | 20-47

## Slide 7
THREE-PHASE SYSTEM SLURRY TECHNOLOGY
Combination of homogeneous and heterogeneous catalysis advantages
+ Heat and mass transfer from the catalyst grain by the liquid medium
+Use of undiluted feed
Catalysis in three-phase systems
(slurry technologies)
DME production
Conversion СО: 30-56% mass.
Selectivity on DME: 91% mass.
DME in product : 95%
Catalyst productivity
– 0,14-0,67 kg/kg(kat)*h
.
Olefins production
DME conversion : 73% mass.
Selectivity on C2-C6: >80% mass.
Ethylene + Propylene : 95%

## Slide 8
Mixing (dissolution)
Oil fractions
Polymer wastes
Dissolved (solubilized) wastes
Catalytic cracking
Motor fuels
Feedstock for petrochemistry
Polymers and polymer wastes:
Polyethylene (PE);
Polypropylene (PP);
Polystyrene (PS);
Poly(ethylene terephthalate)
Oil fractions:
Light gas oil;
Heavy gas oil;
Vacuum distillate
MAIN ADVANTAGES
- Surplus production of motor fuels and petrochemical products;
- Relatively low capital costs due to potential of application of the technology at existing catalytic cracking units
Polymer wastes for production of motor fuels and petrochemical feedstock